PRODUCT:		 	EP Base Oil

DATE OF REVISION: 	08-04-11

ISSUE DATE: 		12-15-06

MANUFACTURER:		ECO-PAK LLC

SELMA, IN

IN CASE OF EMERGENCY CALL INFOTRAC: 1-800-535-5053

- PRODUCT IDENTIFICATION

TRADEMARK:		EP Base Oil

SYNONYMS:		Petroleum Distillate & Emulsifier

CHEMICAL FAMILY: 	Petroleum Hydrocarbon Oil

- HAZARDOUS INGREDIENTS

OSHA REGULATED COMPONENTS

CHEMICAL INGREDIENTS	 CASE NO.	WT%	EXPOSURE LIMITS

Light Paraffin Oil Distillate and Emulsifiers	Mixture	100	  	No Specific Limit

Maximum of 1 ppm Ethylene Oxide (EO) (75-21-8) may be present in the product.

The OSHA PEL and SCGIH TLV for EO is 1 ppm.

- EFFECTS OF OVEREXPOSURE:

Harmful or fatal if swallowed.  Pulmonary aspiration hazard if swallowed and/or vomiting occurs – can enter lungs and cause damage. Excessive exposure may cause irritation to eyes, nose, and throat.  No acute effects expected to be twice exposure limit.  Contact with skin is practically non-toxic if absorbed may result in mild irritation with prolonged or repeated contact.

- EMERGENCY FIRST AID

Call a poison control center or doctor immediately for treatment advice.

IF SWALLOWED:

Have person sip a glass of water if able to swallow. Do not induce vomiting unless told to do so by a poison control center or doctor. Do not give anything by mouth to and unconscious person

IF ON SKIN OR CLOTHING:

Take off contaminated clothing Rinse skin immediately with plenty of water for 15-20 minutes.

IF INHALED:

Move person to fresh air. If person is not breathing, call 911 or an ambulance, and then give artificial

respiration, preferably mouth to mouth if possible.

IF IN EYES:

Hold eye open and rinse slowly and gently with water for  15-20 minutes. Remove contact lenses if

present, after the first 5 minutes, then continue rinsing eye. Have the product container with you when

calling a poison control center of doctor, or going for treatment.

- REACTIVITY DATA

STABILITY:	Stable

CONDITIONS TO AVOID:	Excessive heat

POLYMEMRIZATION:				Will Not Occur

CONDITIONS TO AVOID: 			None known

INCOMPATIBLE MATERIALS: 			Strong oxidizing agents

HAZARDOUS DECOMPOSTION PRODUCTS: 	Combustion may produce carbon monoxide and asphyxiates.

- PHYSICAL PROPERTIES

APPEARANCE: 			 	clear to light amber, may be dyed blue

ODOR:				 	Little Odor

BOILING POINT:		 	>200 degrees Fahrenheit

MELTING POINT:		 	Not Available

VAPOR PRESSURE:		 	Not Available

SPECIFIC GRAVITY: 		 	0.899

VAPOR DENSITY: 		   	Not Available

% VOLATILE (BY VOL):	 		NIL

OCTANOL/H20 PARTITION COEF:	Not Applicable

pH:					Not Available

SATURATION IN AIR (BY VOL):		Not Applicable

EVAPORATION RATE:			(Ethyl Ether=1) >1

- NFPA HAZARD RATING (National Fire Protection Association)

Fire: 			Slight: No hazard beyond that of ordinary combustible material.

- FIRE AND EXPLOSION HAZARD INFORMATION

FLASHPOINT:				> 200 degrees Fahrenheit

SLAMMABLE LIMITS (% BY VOL):	Not Established

AUTOIGNITION TEMP:			Not Established

DECOMPOSTION TEMP:			Not Established

FIRE FIGHTING:	Wear self- contained breathing apparatus when fire fighting in confined space.

EXTINGUISHING MEDIA:	Carbon dioxide, dry chemical and chemical foam or water fog.

HAZARD:	Can be made to burn (Flash point greater than 200 degrees Fahrenheit)

- SPECIAL PRECAUTIONS

HANDLING AND STORAGE/OTHER:

Maintain good housekeeping practices and clean up spills promptly. NFPA Class IIIB storage. Never

siphon by mouth,. Avoid prolonged or repeated contact with skin. Wash thoroughly after handling.

- SPECIAL PROTECTION INFORMATION

Engineering controls are not usually necessary, if good hygiene practices are strictly followed.  Before eating, drinking, or smoking, wash face and hands thoroughly with soap and water. Wear impervious gloves and protective gear if prolonged contact is unavoidable. Launder soiled clothes. Respiratory protection is not normally necessary. However, if product is heated or misted, use MIOSH certified respiratory protection.

- SPILL OR LEAK PROCEDURES

SPILL OR LEAK: 	Contain spill, cover with inert absorbent and transfer to waste disposal container. Aquatic toxicity: Not determined.

WASTE DISPOSAL:	Disposal must be mad in accordance with applicable governmental regulations. Do not flush to drain/storm sewer.

- REGULATORY INFORMATION

COMPOUNDS WHICH REQUIRE REPORTING UNDER SARA TITLE III

Sara Regulated Compounds 		Section 			CAS NO. 	Percent

Residual Ethylene Oxide		302/304		75-21-8		0.001

Glycol Ethers				311 			75-21-8		>0.1

California Prop. 65: The following detectable components of this product are substances, or belong to classes of substances, known to the state of California to cause cancer and/or reproductive toxicity.

Residual Ethylene Oxide		302/304		75-21-8		0.001

The recommendation for safe handling and protection procedures is believed to be generally suitable for the standard used of this compound. However, each user should identify his intended uses of this material and determine whether they are appropriate, all data included in this document is released as typical values and should not be utilized to determine the suitability of this material for a particular use or purpose.  No warranty, either expressed or implied, is hereby made, nor do we give permission, inducement, or recommendations to practice any patented invention without a license. All data is offered for consideration, investigation and verification purposes only.

ECO-PAK LLC

SELMA, INDIANA 47383

# Text boxes

MATERIAL SAFETY DATA SHEET